## Slide 1: Process Overview and Technology for Renewable Diesel
Presentation Date: 21st June 2022
Presentation: Virtual
Authors: Garry Jacobs and Cathleen Shargay, Fluor Corp.

## Slide 2
CRACK EXTENDED CIRCUMFERENTIALLY 10” IN BOTH DIRECTIONS
Source: REFIN-COR 2004F5.7-33.
WASH WATER CONNECTION
LOCATION OF LEAK
Safety Topic Thermal Fatigue
WASH WATER 140°F
HPHS VAPOR 410°F
This heat is stressful!

## Slide 3
Safety Topic Thermal Fatigue

## Slide 4
Economics
Impacts of Feedstock Properties
Facility
Integration
and Modularization
Feedstocks
Processing Steps
agenda

## Slide 5: SHOW ME THE MONEY!
Diamond Green Diesel Facility
Approx $600MM Capital Cost
  Construction through current capacity
  Approx. 18 MBPD
Operating Income >$600MM
  2019: $732MM
  2020: $638MM
Simple payback of <2 years
Economics

## Slide 6: Renewable Product Incentive
($/Gallon) |  | Renewable Diesel |  | Renewable Jet
Feedstock |  | DCO / Tallow | Soybean Oil | DCO / Tallow
Petroleum Value |  | Base | Base | Base - $0.06
Renewable Fuel Standard (RIN) Value | Mandate for blending renewable fuels; credits per gallon blended | $0.83 | $0.83 | $0.78
Low Carbon Fuel Standard (LCFS) Value (CA) | Credit based on Carbon Intensity (CI) of feedstock and process | $1.76 | $1.31 | $1.62
Blender’s Tax Credit (BTC) | $1/Gal incentive for blending to diesel pool | $1.00 | $1.00 | $1.00
Total Incentive |  | $3.59 | $3.14 | $3.34
Source : OPIS – 06 Feb 20 Los Angeles Closing Prices and in-house estimates
$2.54 | $2.54 | $2.54
$0.71 | $0.53 | $0.66
$1.00 | $1.00 | $1.00
$4.25 | $4.07 | $4.14
Source : In-house estimates for Jun 22
↑206% | ↑206% | ↑206%
↓60% | ↓60% | ↓60%
↔ | ↔ | ↔
↑18% | ↑30% | ↑24%

## Slide 7: Renewable Diesel Revenue
Source: (1) S. Irwin, Illinois farmdoc daily (11): 17
Biodiesel use is limited by blending constraints, which effectively caps demand.
ULSD Price
BTC
0.2 D4 RIN
LCFS Credit
Biodiesel Price
Renewable Diesel Price
LOW MARGIN POTENTIAL
HIGH MARGIN POTENTIAL
1.5 D4 RIN
Soy FAME Cost 7.50 lb/Gal + $0.60(1)

## Slide 8
Economics
Impacts of Feedstock Properties
Facility
Integration
and Modularization
Feedstocks
Processing Steps
agenda

## Slide 9: Renewable Feed Stocks
Range of potential feed stocks includes:
  Vegetable oils (e.g., distiller’s corn oil – DCO)
  Animal fats and greases
  Waste oils (e.g., used cooking oil – UCO)
These fats, oils and greases are all triglycerides…
Animal or vegetable, but no minerals…

## Slide 10: Free Fatty Acid (FFA) Nomenclature
FFA (wt%) |  | Soybean Oil |  | DCO |  | Beef Tallow |  | Poultry Fat |  | Pork Grease |  | UCO | 
C12- |  | -- |  | -- |  | -- |  | 1.0 |  | -- |  | -- | 
C14:0 | C14:1 | 0.1 | -- | -- | -- | 3.5 | 0.5 | 1.0 | -- | 1.5 | -- | 0.6 | --
C15:0 | C15:1 | -- | -- | -- | -- | 1.0 | -- | -- | -- | -- | -- | -- | --
C16:0 | C16:1 | 10.6 | -- | 15.5 | -- | 27.0 | 2.5 | 23.0 | 5.0 | 25.5 | 2.5 | 12.9 | 1.0
C17:0 | C17:1 | -- | -- | -- | -- | 2.5 | 0.5 | -- | -- | 0.5 | -- | -- | --
C18:0 | C18:1 | 4.1 | 23.0 | 2.2 | 26.0 | 22.0 | 36.5 | 5.5 | 40.0 | 17.0 | 40.0 | 6.1 | 35.8
C18:2 | C18:3 | 54.5 | 7.2 | 55.0 | 1.3 | 2.5 | 0.5 | 21.0 | 2.5 | 12.0 | 1.0 | 39.0 | 3.9
C20:0 | C20:1 | 0.3 | -- | -- | -- | -- | 0.5 | -- | 0.5 | -- | 1.5 | 0.7 | --
C22+ |  | 0.2 |  | -- |  | -- |  | -- |  | -- |  | -- | 
1
14
0 Double Bonds
1 Double Bond
2 Double Bonds
16
1
18
1
O-CHEM FLASHBACK

## Slide 11: Renewable Feedstocks – Typical Free Fatty Acid (FFA) Profiles
FFA (wt%) |  | Soybean Oil |  | DCO |  | Beef Tallow |  | Poultry Fat |  | Pork Grease |  | UCO | 
C12- |  | -- |  | -- |  | -- |  | 1.0 |  | -- |  | -- | 
C14:0 | C14:1 | 0.1 | -- | -- | -- | 3.5 | 0.5 | 1.0 | -- | 1.5 | -- | 0.6 | --
C15:0 | C15:1 | -- | -- | -- | -- | 1.0 | -- | -- | -- | -- | -- | -- | --
C16:0 | C16:1 | 10.6 | -- | 15.5 | -- | 27.0 | 2.5 | 23.0 | 5.0 | 25.5 | 2.5 | 12.9 | 1.0
C17:0 | C17:1 | -- | -- | -- | -- | 2.5 | 0.5 | -- | -- | 0.5 | -- | -- | --
C18:0 | C18:1 | 4.1 | 23.0 | 2.2 | 26.0 | 22.0 | 36.5 | 5.5 | 40.0 | 17.0 | 40.0 | 6.1 | 35.8
C18:2 | C18:3 | 54.5 | 7.2 | 55.0 | 1.3 | 2.5 | 0.5 | 21.0 | 2.5 | 12.0 | 1.0 | 39.0 | 3.9
C20:0 | C20:1 | 0.3 | -- | -- | -- | -- | 0.5 | -- | 0.5 | -- | 1.5 | 0.7 | --
C22+ |  | 0.2 |  | -- |  | -- |  | -- |  | -- |  | -- | 
Sources: (1) (2) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801.
(1)
(1)
(2)
(2)
(2)
(3)

## Slide 12: Renewable Diesel… IT’S ONLY NATURAL
FFA (wt%) |  | Soybean Oil |  | DCO |  | Beef Tallow |  | Poultry Fat |  | Pork Grease |  | UCO | 
C12- |  | -- |  | -- |  | -- |  | 1.0 |  | -- |  | -- | 
C14:0 | C14:1 | 0.1 | -- | -- | -- | 3.5 | 0.5 | 1.0 | -- | 1.5 | -- | 0.6 | --
C15:0 | C15:1 | -- | -- | -- | -- | 1.0 | -- | -- | -- | -- | -- | -- | --
C16:0 | C16:1 | 10.6 | -- | 15.5 | -- | 27.0 | 2.5 | 23.0 | 5.0 | 25.5 | 2.5 | 12.9 | 1.0
C17:0 | C17:1 | -- | -- | -- | -- | 2.5 | 0.5 | -- | -- | 0.5 | -- | -- | --
C18:0 | C18:1 | 4.1 | 23.0 | 2.2 | 26.0 | 22.0 | 36.5 | 5.5 | 40.0 | 17.0 | 40.0 | 6.1 | 35.8
C18:2 | C18:1 | 54.5 | 7.2 | 55.0 | 1.3 | 2.5 | 0.5 | 21.0 | 2.5 | 12.0 | 1.0 | 39.0 | 3.9
C20:0 | C20:1 | 0.3 | -- | -- | -- | -- | 0.5 | -- | 0.5 | -- | 1.5 | 0.7 | --
C22+ |  | 0.2 |  | -- |  | -- |  | -- |  | -- |  | -- | 
Sources: (1) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801.
(1)
(1)
(2)
(2)
(2)
(3)

## Slide 13: Renewable Jet – LET’S GET CRACKIN’
FFA (wt%) |  | Soybean Oil |  | DCO |  | Beef Tallow |  | Poultry Fat |  | Pork Grease |  | UCO | 
C12- |  | -- |  | -- |  | -- |  | 1.0 |  | -- |  | -- | 
C14:0 | C14:1 | 0.1 | -- | -- | -- | 3.5 | 0.5 | 1.0 | -- | 1.5 | -- | 0.6 | --
C15:0 | C15:1 | -- | -- | -- | -- | 1.0 | -- | -- | -- | -- | -- | -- | --
C16:0 | C16:1 | 10.6 | -- | 15.5 | -- | 27.0 | 2.5 | 23.0 | 5.0 | 25.5 | 2.5 | 12.9 | 1.0
C17:0 | C17:1 | -- | -- | -- | -- | 2.5 | 0.5 | -- | -- | 0.5 | -- | -- | --
C18:0 | C18:1 | 4.1 | 23.0 | 2.2 | 26.0 | 22.0 | 36.5 | 5.5 | 40.0 | 17.0 | 40.0 | 6.1 | 35.8
C18:2 | C18:1 | 54.5 | 7.2 | 55.0 | 1.3 | 2.5 | 0.5 | 21.0 | 2.5 | 12.0 | 1.0 | 39.0 | 3.9
C20:0 | C20:1 | 0.3 | -- | -- | -- | -- | 0.5 | -- | 0.5 | -- | 1.5 | 0.7 | --
C22+ |  | 0.2 |  | -- |  | -- |  | -- |  | -- |  | -- | 
Sources: (1) (2) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801.
(1)
(1)
(2)
(2)
(2)
(3)

## Slide 14
Economics
Impacts of Feedstock Properties
Facility
Integration
and Modularization
Feedstocks
Processing Steps
agenda

## Slide 15: Block Flow Diagram
Hydrogen Plant
PSA Unit
Compression and H2S Scavenger
Salt Driers
Waste Water
Sour Water
Natural Gas
Renewable Diesel Sales
Compression
Hydrogen
Pre- Treatment
H.P. Purge
Off-Gas & LPG
Renewable Naphtha
(1) Can be configured to produce Jet or Diesel
Renewable Diesel Unit(1)

## Slide 16: Reaction Pathways
Produces H2O
High yield, high H2 consumption
CH2 – O – CO – C17H33
CH – O – CO – C17H33
CH2 – O – CO – C17H33
3H2
CH2 – O – CO – C17H35
CH – O – CO – C17H35
CH2 – O – CO – C17H35
3H2
3C17H36 + 3CO2
Decarboxylation
3C17H35COOH + C3H8
3H2
Decarbonylation
3C17H36 + 3H2O + 3CO
9H2
Hydrodeoxygenation
3C18H38 + 6H2O
DCO with Reverse Water Gas Shift
Methanation
  Lower yield, high H2 consumption, methane production
CO2 + H2 ↔ CO – H2O
CO + 3H2 → CH4 + H2O
Produces CO and CO2
  Lower yield, lower H2 Consumption

## Slide 17: Chemical Hydrogen Consumption and Heat Release
 | Petroleum Hydroprocessing(1) |  | 100% Renewable Diesel(2) | 
 | ULSD HDT | Gas Oil HCK | Soybean Oil (100% HDO) | Beef Tallow (100% HDO)
Chemical H2 Consumption (SCFB) | 300 – 1100 | 1500 – 2500 | 2300 | 1900
Heat Release (BTU/SCF H2) | 70 | 60 | 106 | 97
Heat Release (MBTU/BBL) | 21 – 77 | 90 – 150 | 244 | 184
Sources: (1) DIPPR Database V12.0. (2) Hydroprocessing: Hydrotreating & Hydrocracking, Colorado School of Mines
244 | 184
2x to 3x higher than petroleum hydroprocessing!
!

## Slide 18: Hydrogen Impact on Carbon Intensity
Hydrogen production is a significant fraction of the carbon intensity of Renewable Diesel
Reducing the carbon intensity of hydrogen production
 | Carbon Intensity g CO2e / MJ
2022 CA LCFS for Diesel | 90
Currently Blended Renewable Diesel | 34
SMR Hydrogen Content of Renewable Fuel | 12
Basis: 100% HDO reaction for Renewable Diesel from soybean oil. Hydrogen carbon intensity for natural gas via SMR.

## Slide 19: Hydrogen Production with Renewable Diesel Byproducts
Hydrogen Plant
PSA Unit
Compression and H2S Scavenger
Salt Driers
Waste Water
Sour Water
Natural Gas
Renewable Diesel Sales
Compression
Hydrogen
Pre- Treatment
H.P. Purge
Off-Gas & LPG
(1) Can be configured to produce Jet or Diesel
Renewable Diesel
Incorporate SMR carbon capture into graphic or at least into script.
Updates:
If offgas/naphtha yields present, potentially quantify extent of hydrogen production that could be achieved from these sources.
Renewable Feedstock
Renewable Naphtha
Renewable Diesel Unit (1)

## Slide 20: Hydroisomerization Section – NO MSG ADDED
Reactor environment may be sweet or sour
  Sour  Base metal catalyst
    Allows reuse of existing single-stage hydroprocessing units (e.g., DHTs, GOHTs)
  Sweet  Noble metal catalyst
    Best suited for two-stage hydroprocessing units
    Facilitate production of arctic-grade diesel and/or renewable jet
HI catalysts are bi-functional, with acid and metal sites
  Potential for “runaway”…need to design accordingly
Hydroisomerization is hydrocracking
Sources:
(1) Handbook of Commercial Catalysts, H.F. Rase, CRC Press, 1st ed.
(2) PFD Adapted from U.S. Patent 8,329,967

## Slide 21: Hydroisomerization
CARB DIESEL SUMMER
CARB DIESEL WINTER
nC16
ARCTIC DIESEL WINTER
-30
We’re all the same… but different
Sources: (1) Adapted from Fuel 209 (2017) 521-528. (2) API Technical Databook – Procedure 2B14.2.
nC18
83

## Slide 22: Renewable Feedstocks
Property | Soybean Oil | DCO | Beef Tallow | Poultry Fat | Pork Grease | UCO
Sp.Gr. @ 15°C | 0.92 – 0.93 | 0.92 (25°C) | 0.86 (100°C) | 0.92 | 0.86 (100°C) | 0.88 – 0.92
Sulfur (ppmw) |  |  | 30 | 60 | 70 | 4 – 1300
Nitrogen (ppmw) |  |  | 200 | 500 | 400 | 25 - 152
Chlorides (ppmw) | …Samples need to be analyzed… |  |  |  |  | 
FFA (wt%) | < 0.05 | 9 - 12 | 1 - 35 | 15 | 1 - 4 | 
TAN (mg KOH/g) |  | 19 - 23 |  |  |  | 0.3 - 10
Iodine Value | 133 | 112 - 130 | 38 - 45 | 58 - 67 | 50 - 77 | 
Viscosity (cSt @ T) | 55 (25°C) | 31 – 56 (40°C) |  |  |  | 31 – 49 (40°C)
Pour Point (°F) | 3 - 10 | 14 - 23 | 80 - 95 | 70 - 80 | 80 - 86 | 
Sources: (1) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801. (4) Vegetable Oils in Food Technology: Composition, Properties and Uses, 2nd ed. (5) InKemia SDS: Distillers Corn Oil (v1.0) (6) Chemical technology and analysis of oils, fats, and waxes, 3rd ed.
(1)
(1,5)
(1,2,6)
(1,2,6)
(1,2)
(3,4)
How typical…

## Slide 23: but don’t get burned by a bad tan
Source: Adapted from U.S. Patent 8,329,967

## Slide 24: THE USUAL “ACIDIC” SUSPECTS
Property | Soybean Oil | DCO | Beef Tallow | Poultry Fat | Pork Grease | UCO
Sp.Gr. @ 15°C | 0.92 – 0.93 | 0.92 (25°C) | 0.86 (100°C) | 0.92 | 0.86 (100°C) | 0.88 – 0.92
Sulfur (ppmw) |  |  | 30 | 60 | 70 | 4 – 1300
Nitrogen (ppmw) |  |  | 200 | 500 | 400 | 25 - 152
Chlorides (ppmw) | …Samples need to be analyzed… |  |  |  |  | 
FFA (wt%) | < 0.05 | 9 - 12 | 1 - 35 | 15 | 1 - 4 | 
TAN (mg KOH/g) |  | 19 - 23 |  |  |  | 0.3 - 10
Iodine Value | 133 | 112 - 130 | 38 - 45 | 58 - 67 | 50 - 77 | 
Viscosity (cSt @ T) | 55 (25°C) | 31 – 56 (40°C) |  |  |  | 31 – 49 (40°C)
Pour Point (°F) | 3 - 10 | 14 - 23 | 80 - 95 | 70 - 80 | 80 - 86 | 
(1)
(1,5)
(1,2,6)
(1,2,6)
(1,2)
(3,4)
Sources: (1) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801. (4) Vegetable Oils in Food Technology: Composition, Properties and Uses, 2nd ed.(5) InKemia SDS: Distillers Corn Oil (v1.0) (6) Chemical technology and analysis of oils, fats, and waxes, 3rd ed.

## Slide 25: Metallurgy – Impact of Water, CO2, and Chlorides
Need to redraw PFD based on information disclosed in U.S. Patent 8329967.
Eliminate steam heaters…
Source: Adapted from U.S. Patent 8,329,967

## Slide 26: Renewable Feedstocks
Property | Soybean Oil | DCO | Beef Tallow | Poultry Fat | Pork Grease | UCO
Sp.Gr. @ 15°C | 0.92 – 0.93 | 0.92 (25°C) | 0.86 (100°C) | 0.92 | 0.86 (100°C) | 0.88 – 0.92
Sulfur (ppmw) |  |  | 30 | 60 | 70 | 4 – 1300
Nitrogen (ppmw) |  |  | 200 | 500 | 400 | 25 - 152
Chlorides (ppmw) | …Samples need to be analyzed… |  |  |  |  | 
FFA (wt%) | < 0.05 | 9 - 12 | 1 - 35 | 15 | 1 - 4 | 
TAN (mg KOH/g) |  | 19 - 23 |  |  |  | 0.3 - 10
Iodine Value | 133 | 112 - 130 | 38 - 45 | 58 - 67 | 50 - 77 | 
Viscosity (cSt @ T) | 55 (25°C) | 31 – 56 (40°C) |  |  |  | 31 – 49 (40°C)
Pour Point (°F) | 3 - 10 | 14 - 23 | 80 - 95 | 70 - 80 | 80 - 86 | 
Impact Heat Transfer, Hydraulics, Storage, and Winterization
(1)
(1,5)
(1,2,6)
(1,2,6)
(1,2)
(3,4)
Sources: (1) Bailey’s Industrial Oil and Fat Products, 7th ed. (2) Food Processing – Principles and Applications, 2nd ed. (3) Bioresource Technology 100 (2009) 5796-5801. (4) Vegetable Oils in Food Technology: Composition, Properties and Uses, 2nd ed.(5) InKemia SDS: Distillers Corn Oil (v1.0) (6) Chemical technology and analysis of oils, fats, and waxes, 3rd ed.
This is heavy stuff

## Slide 27: Sulfur
Sources: (1) U.S. Patent Application 2019/0359901. (2) CARB LCFS Tier 2 Pathway Application No. B0054.
  Facility integrated with refinery
    Sources:
      Sour water from another hydroprocessing unit(1)
      Refinery hydrogen stream containing H2S(2)
    Disposal: Sulfur plant
      Challenge: Comingled CO2 may detrimentally impact required Reaction Furnace temperature.
Gotta have it
  Standalone facility
    Source: Sulfiding agent
      (e.g., DMDS or TBPS)
    Disposal:
      Iron scavenger
        Caustic scrubbing uneconomical due to high CO2 content
      Wastewater treatment
Sulfur content of most feeds is quite low
  Metal-sulfided HDO catalysts need H2S to avoid reduction
  H2S is comingled with CO and CO2
Sulfur Management
Notes: .

## Slide 28: Utilities THE CHALLENGES OF GOING SOLO
Steam
  Demand
    Needed for feedstock unloading, storage, and handling (seasonal variation)
    Turbine drivers – depending on the source of electric power
  Supply
    Hydrogen plant
    Waste heat production
Hydrogen
  Accommodate feedstock and production variability
    Inter-related with steam production
Flare
  Automatic depressurization likely needed for hydroisomerization catalyst
    Due to runaway potential

## Slide 29: Thank You